## Slide 1
Department of Electrical and Electronic Engineering
Student Name: Zifan Xu (20719616)
Supervisor: Chiew-Foong Kwong
Whole-Body Control for a Mobile Manipulator
with QP + Reinforcement Learning
RoArm-M3 demo: MTC planning and camera-guided grasping
Project overview
This poster presents the RoArm-M3 motion-planning and vision-guided grasping components of the wider whole-body control project. A fixed camera provides a target pose; eye-to-hand calibration maps it into the robot base frame. MoveIt Task Constructor (MTC) plans the manipulation stages, while measured joint feedback updates the robot state.
Demo pipeline
01
Camera
Target observation
→
02
Calibration
Camera → base
→
03
MTC
Approach + grasp
→
04
RoArm-M3
Execute + feedback
Control path: MoveIt 2 / MTC → ros2_control → serial driver → RoArm-M3. Measured joint angles → /joint_states → TF.
Existing hardware setup
RoArm-M3 with AprilTag at the gripper for eye-to-hand calibration.
MoveIt Task Constructor plan
Provided MTC Task Tree: one displayed Cartesian Path solution. This image does not show grasp execution.
Grasp trials
17 / 20
successful trials · 85%
95% exact CI: 62.1–96.8% | an irregularly shaped part; randomized starts; real hardware
ESP32 LSTM controller; 30 demonstrations; one evaluated checkpoint.
Complete TF tree
Original ROS view_frames output. The tree shows frame connectivity; calibration accuracy needs separate validation.
Accuracy
End-effector position: 2.96 mm mean ± 0.57 mm SD (n=6); held-out split unspecified
Camera reprojection: 0.30 px mean (n=25); calibration-set fit
Camera-to-robot alignment: 1.18 mm RMS (n=12); correspondence fit
Trajectory tracking: 2.9 mm MAE; sample count not reported